## Slide 1: A multi-criteria contract manufacturing approach in a stochastic manufacturing environment SMMSO, Volos, 2015
Catherine Decouttere & Nico J. Vandaele, Catholic University of Leuven, GSK Research Chair
Gerd J. Hahn, GGS Heilbronn & Torben Sens, LHConsulting
Notes: Not mainstream: apply stochastic models for planning
Originates at industry-university link: spin-off; GSK on supply chain design, AC on corporate S&OP planning
Three methodological blocks: milp (gerd and torben) , stoch (nico) and dea (catherine): links and framework: is it feasible

## Slide 2: Context of this presentation
Modelling and analysis is the main focus of the field.
Applications for planning have received much less attention.
Implementations of these planning approaches are even more scarce.
Sales and Operations Planning (S&OP) is a mid-term business process considering operational, financial and general Key Performance Indicators (KPI’s).
Relation with previous work:
  Stochastic/deterministtic model has been presented in SMMSO 2013
  Now embed the stochastic models in a scenario framework
  Partially desktop example in the area of contract manufacturing
  First application is underway under a university-industry contract

## Slide 3: Objectives of this presentation
Motivate the issue of contract manufacturing and explain its relevance and impact on strategic-tactical planning
Introduce a DEA-based approach for robust multi-criteria decision-making on top of a combined stochastic MILP model to “evaluate” strategic decisions at the tactical level
In higher level decision making, we typically face:
  Different stakeholders with different goals which induce different KPI’s
  Decisions which induce design parameters
  Environmental events which induce scenarios
In addition, the approach must be pragmatic and intuitive. It must have communication capabilities.
The example of contract manufacturing is used to illustrate this view point, partially based on a real life case, partially desk-top.
Notes: DEA: relates anastacia multiple stakeholders in train traffic announcements, kpî’s come in

## Slide 4: Contribution
Observations
Context: (S&OP)
Example: contract manufacturing (CM)
Planning is organized in time buckets
Deterministic logic BUT
Transient issues and dynamics are omnipresent
System behavior is a continuous phenomenon
Stochastic logic, BUT
Decisions are taken at specific moments and for specific periods
Combining stochastic and deterinistic modeling
Induces multiple system settings, controllable and uncontrollable
Results in multiple criteria decision making (DEA)
Notes: Refinements wrt SMMSO 13, DEA is the main addition
DEA can be used to evaluate models:
Manufacturing improvements  R&D
Supply chain: GSK
S&OP

## Slide 5: S&OP: a landscape of multiple KPI’s
High
Profitability
Low
Costs
Low Unit
Costs
High
Throughput
Less
Variability
High
Utilization
Low
Inventory
Quality
Product
High
Sales
Many
products
Fast
Response
More
Variability
High
Inventory
Low
Utilization
Short
Cycle Times
High Customer
Service
Modelling tradeoffs is key in S&OP.
However, we will never be able to include all KPI’s in one single model.
Notes: Model based
Non model based

## Slide 6: S&OP: a flow model to balance supply and demand
Utilization
Lead times
Inventories
Throughputs
SKU
Families
BOM
Demand Shaping
Phasing in/out
Mix
Optimal Lot size
Demand
Resources
Processes
Setups
Availability
Alternatives
Make or buy
Breakdowns
Scrap, rework
Supply
+
+
Randomness
Variabilities
Heterogeneity
Complexity
Demand
Supply
Service levels
+
Notes: Add refenrence

## Slide 7
Contract Manufacturing
In house manufacturing
Demand
Leadtime/Inventory
S&OP: a model to connect multiple periods

## Slide 8: Empirical evidence motivates investigation into the subject of contract manufacturing (CM) and its implications on production management
The New York Times, May 18, 2014 (edited)
The New York Times, January 21, 2012 (edited)
General observable trends
USD 342 bn in global sales for the top 25 CMs in 2013, ~30% of the total EMS1 manufacturing market
US electronics CM market to grow by 39% from 2012 to 2018
Global pharmaceutical CM market with CAGR of ~7% until 2017 with expected market size of USD 18.5 bn
Further industries with similar trend to reduce internal value added: automotive, aerospace, food production, personal care
Notes: Quellen: http://mfgmkt.com/mmi-articles.html, http://www.statista.com/statistics/239692/projected-size-of-the-us-electronics-contract-manufacturing-market/, http://de.slideshare.net/FrostandSullivan/global-pharmaceutical-contract-manufacturing-market-injectable-dose-formulations-will-likely-spur-the-growth-of-cm-os

## Slide 9: We consider the strategic-tactical issue of contract manufacturing in a stochastic manufacturing environment
Turnkey (finished goods) CM in contrast to consignment (components) CM
On-demand manufacturing of variable production volumes given agreed volume corridors and fixed service level agreements
CM with benefits (capacity flexibility, risk transfer) and costs/risks (margin of contractor, quality/reputational threats, IP infringement,…)
Setting
Decision problem
Strategic-tactical issue of sourcing is multi-criteria decision problem involving quantitative and qualitative factors: throughput, service, cost, risk, …
Sourcing decisions with massive impact on operational KPIs at shop floor level (lead time, WIP, etc.)
Coordination role of tactical planning: volume/mix decisions impact batch sizes, capacity buffers and lead times (workload-dependent and non-linear)
How to deal with contract manufacturing in a stochastic manufacturing environment?

## Slide 10: Existing literature does not cover a combined robust approach for tactical planning of stochastic manufacturing systems with contract manufacturing options
  Clearing Functions: Approximation of non-linear relationship between workload and lead time, linearization in APP (single model approach)
Tactical Planning
  Karmarkar (1987, MS)
  Missbauer (2011, IJPE)
  Selcuk et al. (2008, IIE)
Simulation
  Iterative parameter fine-tuning and system evaluation with Discrete Event Simulation (DES)
  Almeder et al. (2009, OR Spec)
  Gansterer et al. (2014, IJPE)
Analytical
  Multi-model approaches: Iterative solution procedure through analytic approximation of workload-dependent lead times
  Jansen et al. (2013, OR Spec)
  Hahn et al. (2012, OR Proc)
Description
Selective references
  Explicit consideration of subcontracting or capacity management in master planning
Contract Manufactu- ring, Supplier Selection
  Merzifonluolgu et al. (2007, NRL)
  Kim (2003, IJPE)
  Atamtürk/Hochbaum (2001, MS)
  Carravilla/de Sousa (1995, EJOR)
Currently, no combined approach available for robust decision-making accommodating stochastic manufacturing systems and issues of sourcing/contract manufacturing (or S&OP in general)
  Multi-criteria/DEA approaches for structured selection of suppliers
  de Boer et al. (2001, EJPSM)
  Dotoli/Falagario (2012, IJPE)

## Slide 11: A DEA-based approach is used to provide a robust multi-criteria perspective on the contract manufacturing issue
 | M-KPI1 | M-KPI2 | … | M-KPIp | N-KPI1 | N-KPI2 | … | N-KPIq
Scenario 1 |  |  |  |  |  |  |  | 
Scenario 2 |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  | 
Scenario N |  |  |  |  |  |  |  | 
a. Identify stakeholders
TECH
ECON
HUMAN
KPI
…
…
…
…
…
…
…
…
…
b. Define KPIs
Model-based KPIs
Non-model-based KPIs
a. Rank scenarios
Generate/evaluate designs (outsourcing options) and scenarios (uncertain parameters)
b. Select robust designs
1
2
3
Design I
Design II
…
Quantitative Model
(see next slides)
Qualitative Assessment
Notes: Basic idea and approach of the DEA:
1. line up the major stakeholders in the S&OP process 2. derive the KPI's according to these stakeholders, including the metrics used 3. generate scenarios and assess their performance against the metrics of the KPI's; thresholds limit the set of eligible scenarios 4. rank the scenarios in a multi-criteria way 5. make final decision and keep track of some backup scenarios (robustness idea)

## Slide 12: Classical master planning model is enhanced with a queuing networks approach to capture stochastic effects of manufacturing system
APP model
1/5
2
ASQ models per period t = 1..T
…
t = 1
t = 2
t = 3
t = T
3
4
Instruction
Expected inter- arrival times derived from:
  - Production volume
  - Gross capacity
Reaction
  Lead time (per backwards scheduling)
  Capacity buffer (incl. setups and technical failures)
Description
APP: Aggregate Production Planning
Balancing capacity and WIP costs
Managing volume/mix for internal/external production
Anticipation of actual available capacity and lead times
1/5
3
Schematic model representation
ASQ: Aggregate Stochastic Queuing
Stochastic lot-sizing model for job shop (queuing network)
Approximation of operational KPIs
Conducted separately per APP time bucket
Notes: Based on the remarks, we refined the model lead time putting volumes in particular periods
SIPP: stationary independent per period

## Slide 13: A standard APP model is modified to better anticipate actual capacity available and lead times according to production volumes
Aggregate Production Planning model
  Model anticipates actual capacity available and average lead times
  Model considers WIP costs according to lead time
  Objective function minimizes capacity and WIP cost, thereby implicitly minimizing manufacturing lead times
  Binary capacity use offset γ allocates capacity demand to the respective period
  Capacity buffer α accommodates for setup losses and technical failures
capacity cost
WIP cost

## Slide 14: An ASQ model for optimal order batching in a job shop environment is applied to approximate capacity buffer and lead times
Aggregate Stochastic Queuing Model
  Expected weighted lead Time E(Θ) as a function of batch size Q consists of waiting time to batch (wb), waiting time in queue (wq), and setup and processing time (st, pt)
  Constant batch size Q for whole routing is assumed

## Slide 15: A DEA-based approach is used to provide a robust multi-criteria perspective on the contract manufacturing issue
 | M-KPI1 | M-KPI2 | … | M-KPIp | N-KPI1 | N-KPI2 | … | N-KPIq
Scenario 1 |  |  |  |  |  |  |  | 
Scenario 2 |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  | 
Scenario N |  |  |  |  |  |  |  | 
a. Identify stakeholders
TECH
ECON
HUMAN
KPI
…
…
…
…
…
…
…
…
…
b. Define KPIs
Model-based KPIs
Non-model-based KPIs
a. Rank scenarios
Generate/evaluate designs (outsourcing options) and scenarios (uncertain parameters)
b. Select robust designs
1
2
3
Design I
Design II
…
Quantitative Model
(see next slides)
Qualitative Assessment
SOURCE: Vandaele/Decouttere/Lemmens/Bernuzzi (2014, 2015), Advances in Humanitarian Operations, Springer.
Notes: Basic idea and approach of the DEA:
1. line up the major stakeholders in the S&OP process 2. derive the KPI's according to these stakeholders, including the metrics used 3. generate scenarios and assess their performance against the metrics of the KPI's; thresholds limit the set of eligible scenarios 4. rank the scenarios in a multi-criteria way 5. make final decision and keep track of some backup scenarios (robustness idea)

## Slide 16: A numerical example is used to evaluate the combined approach
Case example
Job shop with 12 products from 4 families and 10 machines
Fixed linear routing with 7 or 8 out of 10 machines
Make to order environment
Customer demand is dynamic
Setup times are stochastic
Processing times are deterministic
Regular capacity is 160 hours a month before machine availability
280 hours is max overtime

## Slide 17
Notes: Min max: over de 12 producten een setup met gemiddelde tussen 0.05 en 0.45 en een squared coefficient of variation between 0 en 0,013
Processing time between 0.016 en 0.016 (hier dus deterministisch en voor alle producten gelijk)

## Slide 18: Design options – Scenarios Full factorial design
54 Design – Scenario combinations
Internal controllable factors – Design options |  |  | 
Sourcing option |  | Setup variability | 
Inflexible | specialized in 1 product with limited capacity and low unit costs | Low | x from base case
Flexible | covering all products, higher dedicated capacity, high unit costs | Moderate | 0,3 + 1,2x
Mixed | both are allowed | High | 0,8 + 2x
External factors - Scenarios |  |  | 
Demand variability |  | Demand Seasonality | 
Deterministic | SCV = 0 | Flat | 10% min-max
Moderate | SCV = 1,0 | Fluctuating | 30% min-max
High | SCV = 2,5 |  | 

## Slide 19: DEA Formulation
Problem formulation
LP formulation
Vandaele N., Decouttere C., ‘Sustainable R&D portfolio assessment’, Decision Support Systems, 2012
CCR model: Charnes, Cooper & Rhodes [1978] CRS, Input oriented, Radial
e.r.b. T.T.

## Slide 20: Multi criteria evaluation model: Data Envelopment Analysis (DEA)
Vandaele N., Decouttere C., ‘Sustainable R&D portfolio assessment’, Decision Support Systems, 2012
CCR model: Charnes, Cooper & Rhodes [1978] CRS, Input oriented, Radial
Notes: CCR model: Charnes, Cooper and Rhodes [1978]
  CRS constant returns to scale
  Input oriented
  Radial
BCC model: Banker, Charnes and Cooper [1984]
  VRS variable returns to scale
  Input oriented
  Radial

## Slide 21
Costs
CM volume
Lead times
APP-ASQ model
Numerical example:
inputs and outputs for DEA
Inputs
“efforts”
Outputs
“rewards”
Efficiency?
Technical risk
S&OP stakeholders:
“Become as responsive as possible by using outsourcing for the lowest cost and technical risk”
optimal cost

## Slide 22: APP-ASQ deep dive
Notes: Inflexible: overtime is preferred over cm whilst mixed and flex beat overtime
Mixed turns out to be cheapest
flex: most cost
Lot sizes play a dampening role
Fluct versus flat: more expensive; more on CM

## Slide 23: Multi dimensional efficiency

## Slide 24: Scenario data and efficiency

## Slide 25: Scenario list

## Slide 26: Efficiency analysis
Chart: Scenario
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54
not efficient | 97.8664 | 97.1435 | 94.7172 | 97.9765 | 96.9574 | 94.56 | 97.7109 | 96.8075 | 94.3121 | 54.065 | 52.5694 | 58.2236 | 53.8551 | 52.3563 | 58.0786 | 53.5195 | 59.5755 | 57.8615 | 100 | 99.8266 | 97.0122 | 99.9891 | 95.3655 | 92.3164 | 99.633 | 100 | 93.1888 | 99.8711 | 98.5685 | 96.2452 | 100 | 98.7083 | 96.0798 | 96.4212 | 95.0694 | 92.5025 | 100 | 98.6281 | 95.6102 | 99.7757 | 98.3593 | 95.2062 | 99.4671 | 98.0484 | 94.9008 | 100 | 98.7285 | 96.1371 | 99.8337 | 98.5778 | 95.9919 | 99.551 | 98.2648 | 95.6049
efficient | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100 | 100 | 0 | 100 | 0 | 0 | 100 | 100 | 0 | 100 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0 | 100 | 0 | 0 | 0 | 0 | 0 | 100 | 0 | 0 | 100 | 0 | 0 | 100 | 0 | 0
Inflexible supplier
Flexible supplier
Mixed supplier
Setup variability
LMH
Flat
Fluct
Demand variability
lo
hi
mo
Demand seasonality
Flat
Fluct
lo
hi
mo
Flat
Fluct
lo
hi
mo
lo
hi
mo
lo
hi
mo
lo
hi
mo
Notes: Flow: Over alle periodes kosten minimaliseren (APP)

## Slide 27: Contracted volume versus risk and cost
Mixed supplier
Fluctuating seasonality
Mixed supplier
Flat seasonality
Flex supplier
Flat seasonality
Low demand variability
Flex supplier
Fluct seasonality
Inflex supplier
Flex supplier
Flat seasonality
Mod-Hi demand variability

## Slide 28: Lead time-1 versus risk and cost
Flex supplier
Flat seasonality
Low demand variability
Inflex supplier
Fluct seasonality
Mixed supplier
Flat seasonality
Flex supplier
Flat seasonality
Mod-Hi demand variability
Flex supplier
Fluct seasonality
Inflex supplier
Flat seasonality
Mixed supplier
Fluctuating seasonality

## Slide 29: Conclusions
S&OP
  Stochastic model per period
  Deterministic model connecting the periods
  Non Parametric approach: multiple KPI’s
Illustration by Contract Manufacturing, more widely applicable
Current/Future:
  Refinements
  Convergence
  KPI assessments
  Full real life case
Notes: Case atlas copco.

## Slide 30: Questions? nico.vandaele@kuleuven.be catherine.decouttere@kuleuven.be

## Slide 31
Scenario generation
Demand uncertainties
(market evolution, demand pattern)
Cost of labour
(std, timebank, temp)
Stock policy CC
Production allocation policy
(on time, before)
Source of labour policy
(fraction TB & temp)
Flow model
(monthly, product family)
Financial model AC
Multi criteria evaluation model
(yearly, company level)
WIP cost
PC
HR cost
(std,TB,TMP)
Service level
Responsiveness
Customer Satisfaction
Internal profit
Takt
HR hrs
std & overtime
WIP cost
CC
Data AC
external
decision
calculated
WIP capital cost
flowscen
finscen
DEAscen
Allscen
(flow + fin)
flowfin
datatable
flowDEA
efforts
rewards
finDEA