## Slide 1: Discrete-time analysis of a 4-way-crossing in conveying systems under the dispatching policy round robin
SMMSO 2015
Rimmele, Furmans and Epp

## Slide 2: Outline
Introduction
System description
Discrete-time analysis
  Iterative algorithm
  Cycle time distribution
  Steady-state probabilities
  Service time distribution
  Waiting time distribution
  Interdeparture time distribution
Numerical Study
Conclusion and future work

## Slide 3: Introduction
A 4-way crossing in conveying systems

## Slide 4: Introduction
The dispatching policy round robin
conveying units |  | 
no. | source | drain
1 | 1 | 1
2 | 1 | 2
3 | 2 | 2
4 | 1 | 1
5 | 2 | 1

## Slide 5: System description
interarrival time distribution of queue 1
interarrival time distribution of queue 2
conveying time distribution of queue 2
conveying time distribution of queue 1
INPUT
Tran-Gia (1992)

## Slide 6: System description
waiting time distribution of queue 1
interdeparture time distribution of drain 2
waiting time distribution of queue 2
interdeparture time distribution of drain 1
OUTPUT
Tran-Gia (1992)

## Slide 7: Discrete-time analysis
Iterative algorithm
Initialization
Calculate the cycle time distribution
Calculate the steady-state probabilities
Repeat steps 2-3 until a convergence criterion for the steady-state is fulfilled
Calculate the service time distribution
Repeat steps 2-5 until convergence criterion for the service time is fulfilled
Calculate the waiting time distribution and the inter departure time distribution
Notes: Similar to the approach presented from Tran-Gia (1992), we propose a numerical calculation algorithm based on an alternating evaluation of the cycle time distribution and the state probability vector based on a discrete-time Markov chain. Additionally, we expand this iterative algorithm to calculate the service time distribution, which depends on the steady-state probability 𝑥_(𝑖,0). Starting with an initial service time distribution the algorithm computes the cycle time distribution and the state probability vector iteratively until a convergence criterion for the steady-state is fulfilled. After that, a new service time distribution is calculated and the iterative calculation of 𝑐_(𝑖,𝑚) and 𝑥_𝑖 starts again. This process is repeated until the service time distribution converges. Subsequently, the waiting time distribution, the distribution of the number of customers of a queue and the interdeparture time distribution are computed as performance measures.

## Slide 8: Discrete-time analysis
Cycle time distribution
  Cycle time distribution conditioned on an empty queue where
  Cycle time distribution conditioned on a non-empty queue
  Cycle time distribution of queue
Notes: We initially observe only epochs right before starting the service at queue 𝑖. The time interval between two services at queue 𝑖 is called cycle time. Similar to the approach provided by Tran-Gia (1992), two types of conditional cycle times (𝑚=0,1) at queue 𝑖 can be distinguished, denoted by the random variable 𝐶_(𝑖,𝑚). In the case of 𝑚=0, the cycle time is conditioned on an empty queue 𝑖, whereas in the case of 𝑚=1 queue 𝑖 is non-empty. The number of customers in queue 𝑖 describes the state of the queue at the beginning of a new service interval and is distributed according to 𝑋_𝑖.

## Slide 9: Discrete-time analysis
Steady-state probabilities
  Distribution of the arrival time of the ℎ-th customer
  Group size distribution
  Steady state
Notes: To evaluate the steady-state probabilities, we first determine the group size distribution. We observe at queue 𝑖 a cycle of type 𝑚 and the arrival group of customers arriving in this cycle. The time between the start of an epoch and the arrival epoch oft he ℎth customer in this group is distributed according to this formula. In the case of observing the first arriving customer the distribution is equivalent to the residual interarrival time. Otherwise the fold convolution of the interarrival time distribution is added.
By applying the law of total probability, the distribution of an arrival group in queue 𝑖 during a cycle can be obtained.
Finally, the transition behavior between two consecutive epochs can be deduced. Under the stationary conditions the steady state equations of the Markov chain can be derived.

## Slide 10: Discrete-time analysis
Service time distribution
  Probability that two conveying units from the same source are conveyed consecutively
  Probabilities of shifting
  Service time distribution
Notes: The service time of queue 𝑖 is defined as the time span to serve a customer from queue 𝑖 including the potentially necessary shifting time to switch the server in the right direction to serve the customer. In order to determine the service time, the probability of shifting has to be computed.
Therefore, we calculate the probability that two conveying units from the same source 𝑖 are conveyed consecutively. This corresponds to the probability that the other queue is empty and no unit arrives at this queue during the service of a unit from queue 𝑖, which means that the service time from source 𝑖 is less than the residual interarrival time from the other source. This probability can be calculated by the computed state probability in iteration 𝑛, the service time distribution from the last iteration and the residual interarrival time distribution.
Subsequently, the probabilities of shifting 𝜎_𝑖 for the two sources can be calculated using the transition probability from source 𝑖 to drain 𝑗.
Based on the probability of shifting and the given shifting time, the shifting time distribution can be calculated for both directions. The conveying time distribution is composed of the transition probability and the given times to convey the units in continuous and discontinuous direction, respectively. Thereby, the service time distribution is computed as the convolution of conveying time distribution and shifting time distribution.

## Slide 11: Discrete-time analysis
Waiting time distribution
  Conditional waiting time distribution of the first customer

## Slide 12: Discrete-time analysis
Waiting time distribution
  Conditional waiting time distribution of the -th customer
2
Notes: We can now further generalize the findings to the case of the 𝑙th arriving customer during the observed cycle interval. In comparison to the cases of the first arrival we now consider also the customers that arrive before the customer. In case of non or one customer in the queue, the customer has to wait additional cycles that are needed to serve the waiting customers that arrived before. Otherwise the 𝑙th arriving customer is waiting additional cycles that are needed to serve the already waiting customers and additional cycles to serve the waiting customers that arrived before.
Hence, the probability for the occurrence of the 𝑙th customer is given by this formula
Next, we apply the Bayes’ theorem and the law of total probability to and obtain the waiting time probability of queue 𝑖

## Slide 13: Discrete-time analysis
Inter departure time distribution
  Total inter departure time distribution  According to Grassmann and Jain (1988, 1989) with
      Service time distribution
      Waiting time distribution
      Idle time distribution
  Inter departure time for queue  According to Furmans (2004) with a stochastic split
Notes: To calculate the interdeparture time we combine several existing models. First the total interdeparture time distribution has to be computed according to Grassmann and Jain (1988, 1989). The total interdeparture time distribution depends on the utilization of the system. If the system is highly utilized and customers are waiting in the queue, the interdeparture time intervals are equal to the service time. If the utilization is lower and a server has idle time periods, the time interval between two departures increases by this idle time. The probability of an idle time 𝑘 is equivalent to the probability that both queues are exactly 𝑘 epochs empty. In accordance with Grassmann and Jain (1988), the interdeparture time distribution can be calculated with the idle time distribution, the service time distribution and the waiting time distribution.
Finally, the method of Furmans (2004) to split stochastically is used to calculate the interdeparture time distributions for both drains.

## Slide 14: Numerical study
Parameter settings
Parameter type | Cases | Value
 | 3 | Exponential, Uniform, Gamma
 | 3 | Exponential, Uniform, Gamma
 | 3 | 0.5, 0.75, 0.95
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9
 | 2 | (1,2,1), (2,4,2)
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9
Parameter type | Cases | Value
 | 3 | Exponential, Uniform, Gamma
 | 3 | Exponential, Uniform, Gamma
 | 3 | 0.5, 0.75, 0.95
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9
 | 2 | (1,2,1), (2,4,2)
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9
 | 5 | 0.1, 0.25, 0.5, 0.75, 0.9

## Slide 15: Numerical study
Chart: absolute error [time units]
Chart: relative error [%]
Distribution of the relative and absolute errors for the waiting time of source 1

## Slide 16: Numerical study
Chart: absolute error [time units]
Chart: relative error [%]
Distribution of the relative and absolute errors for the inter departure time of drain 1

## Slide 17: Numerical study
Comparison of round robin and first-in first-out
 |  | round robin |  | first-in-first-out | 
0.5 | 0.1 | 0.6224 | 2.8289 | 0.6295 | 3.3756
 | 0.25 | 0.6566 | 3.0556 | 0.8243 | 4.2133
 | 0.5 | 0.8069 | 3.6133 | 0.9580 | 4.6778
 | 0.75 | 0.8880 | 3.8800 | 0.8243 | 4.2133
 | 0.9 | 0.9369 | 4.0400 | 0.6295 | 3.3756
0.75 | 0.1 | 0.9902 | 3.2778 | 2.0934 | 8.0444
 | 0.25 | 1.2660 | 4.4578 | 2.5568 | 9.6222
 | 0.5 | 1.7205 | 6.1733 | 2.8596 | 10.6200
 | 0.75 | 2.4645 | 8.7089 | 2.5568 | 9.6222
 | 0.9 | 3.5367 | 11.6267 | 2.0934 | 8.0444
0.95 | 0.1 | 1.2927 | 3.9489 | 12.9688 | 40.9267
 | 0.25 | 2.1033 | 6.6689 | 16.0774 | 50.3556
 | 0.5 | 5.6607 | 17.8644 | 18.3352 | 57.1756
 | 0,75 | 15.7522 | 35.6689 | 16.0774 | 50.3556
 | 0,9 | 19.7308 | 36.5911 | 12.9688 | 40.9267
 |  | round robin |  | first-in-first-out | 
0.5 | 0.1 | 0.6224 | 2.8289 | 0.6295 | 3.3756
 | 0.25 | 0.6566 | 3.0556 | 0.8243 | 4.2133
 | 0.5 | 0.8069 | 3.6133 | 0.9580 | 4.6778
 | 0.75 | 0.8880 | 3.8800 | 0.8243 | 4.2133
 | 0.9 | 0.9369 | 4.0400 | 0.6295 | 3.3756
0.75 | 0.1 | 0.9902 | 3.2778 | 2.0934 | 8.0444
 | 0.25 | 1.2660 | 4.4578 | 2.5568 | 9.6222
 | 0.5 | 1.7205 | 6.1733 | 2.8596 | 10.6200
 | 0.75 | 2.4645 | 8.7089 | 2.5568 | 9.6222
 | 0.9 | 3.5367 | 11.6267 | 2.0934 | 8.0444
0.95 | 0.1 | 1.2927 | 3.9489 | 12.9688 | 40.9267
 | 0.25 | 2.1033 | 6.6689 | 16.0774 | 50.3556
 | 0.5 | 5.6607 | 17.8644 | 18.3352 | 57.1756
 | 0,75 | 15.7522 | 35.6689 | 16.0774 | 50.3556
 | 0,9 | 19.7308 | 36.5911 | 12.9688 | 40.9267
Notes: To evaluate the dispatching policy round robin a comparison of the strategies round robin and first-in first-out is conducted. Therefore, the waiting time distribution of source 1 is measured under different parameter settings. This table lists the expected value and 95% quantiles for the waiting time of source 1.
Due to the dispatching policy round robin the server serves the queue that has a smaller throughput more frequently than under the dispatching policy FIFO. So the waiting time of queue 1 for 𝑑_1 less then 0.5 is smaller compared to the dispatching policy first-in first-out.
However, also for 𝑑_1 is equal 0.5 round robin provides better results. This can be explained by the constant service of both queues by round robin.
In the case of a high utilization it should be noted that the capacity of both queues is limited to 20 customers for the policy round robin whereas the capacity for the first-in-first-out is unlimited. This causes a considerable smaller waiting time for a utilization of 95 % using the dispatching policy round robin.

## Slide 18: Conclusion and future work
We developed a model of a 4-way-crossing based on a polling system, in which a single server serves two queues cyclically.
Future work will be dedicated to model further dispatching policies (e.g. exhaustive) based on this approach.
A comparison of different dispatching policies should be considered in more detail.

## Slide 19
Thank you for your attention!

## Slide 20
Karlsruhe Institute for Technology (KIT) Institute for Material Handling and Logistics (IFL)
Postal address Kaiserstr. 12 DE-76128 Karlsruhe
Visitor address Gotthard-Franz-Str. 8, Geb. 50.38 DE-76131 Karlsruhe
Phone +49-721-608-48600 Fax +49-721-608-48629 Email info@ifl.kit.edu
www http://www.ifl.kit.edu

## Slide 21: References
Boxma, J. 1984. Two symmetric queues with alternating service and switching times. Proc. Perf. 409-431.
Furmans, K. 2004. A framework of stochastic finite elements for models of material handling systems. Progress in material handling research: 8. International Material Handling Research Colloquium.
Grassmann, W.K., J.L. Jain. 1988. Numerical solution for the departure process from the GI/G/1 queue. Comput. Opns Res. 15 (3) 293-296.
Grassmann, W.K., J.L. Jain. 1989. Numerical solutions of the waiting time distribution and idle time distribution of the arithmetic GI/G/1 queue. Operations Research 37 (1) 141-150.
Kuehn, J. 1979. Multiqueue systems with nonexhaustive cyclic service. Bell Sysi. Tech. J. 58 671-699.
Manfield, D. R. 1983. Analysis of a polling system with priorities. Proc. GLOBECOM 43 (4).
Matzka, J. 2011. Discrete time analysis of multi-server queueing systems in material handling and service. PhD Thesis. Karlsruhe Institute of Technology
Özden, E. 2011. Discrete time Analysis of Consolidated Transport Processes. PhD Thesis. Karlsruhe Institute of Technology
Schleyer, M. 2007. Discrete time analysis of batch processes in material flow systems. Ph.D. thesis, Institut für Fördertechnik und Logistiksysteme (IFL), University Karlsruhe.
Schleyer, M., K. Furmans. 2007. An analytical method for the calculation of the waiting time distribution of a discrete time G/G/1-queueing system with batch arrivals. OR Spectrum 29 (4) 745-763.
Takagi H. 1986. Analysis of Polling Systems. MIT Press
Tran-Gia, P. 1992. Analysis of polling systems with general input process and finite capacity. IEEE 'Transactions on Communications 40 (2).
Tran-Gia P., T. Raith. 1985. Multiqueue systems with finite capacity and nonexhaustive cyclic service. Proc. Int. Sem. Comput. Networking Perform. Eval. .