## Slide 1: A Simple Model of the Effects of Quality on Market Share and Profitability in Single Stage Manufacturing Systems
Dimitrios Konstantas, Evangelos Grigoroudis, Vassilis S. Kouikoglou and Stratos Ioannidis
Department of Production Engineering and Management
Technical University of Crete, 73100 Chania, Greece
10th Conference on Stochastic Models of Manufacturing and Service Operations

## Slide 2: Motivation
Customer satisfaction has a key-role to market share and therefore to profitability
What is the interaction between customer satisfaction and production systems control?
We examine the case of quality

## Slide 3: Problem description
Single-stage manufacturing system
Make-to-order system (working only when there are unsatisfied orders)
Known and constant market size
Two distinct customer classes: regular and occasional
Customers from both classes place their orders to the system
All waiting customers become unclassified
A satisfied customer becomes a regular customer
A dissatisfied customer becomes an occasional customer

## Slide 4: Customer satisfaction
Outgoing products inspected and graded on the basis of quality
Customer satisfaction depends only on the quality of the item purchased
The higher the item quality level the higher the probability of customer satisfaction
Satisfaction probabilities are independent of past customer states

## Slide 5: Control of production system
Control decision
Selling or scrapping an item just produced
The optimal decision depends on:
The quality level of the item
The number of customers waiting for service
The number of regular customers in orbit
Control target
Maximize the market share and the average profit of the system

## Slide 6: System description
n0
n1
M: Market size
x: regular customers in orbit
y: customers waiting for service
M-x-y: occasional customers
1 : regular customers mean demand rate (Poisson)
2 : occasional customer mean demand rate (Poisson) (1 > 2)
 : mean production rate (Exponential)
i : quality level (i = 0, 1,…, I. quality decreasing as i increases)
pi : production probability of a quality level i item
si : satisfaction probability from the purchase of a quality i item
n2
1-si
si
n1 = x
n2 = M – x – y
n0 = y
n11
n22
Profit and cost parameters
r : profit from selling a product
c : unit rejection cost
b : unit backlog cost per order and per time unit
µ

## Slide 7
System states
The system state is described by the pair (x , y)
State space: Z  {(x, y)|x  0, 1, …, M and y = 0, …, M  x}
Obviously: x + y ≤ M
Control decisions
Selling decision (x, y, i) = 0 , when we decide to scrap the quality level i item just produced, while being in state (x, y)
Selling decision (x, y, i) = 1 , when we decide to sell the quality level i item just produced, while being in state (x, y)

## Slide 8
Events
Order placement by regular or occasional customer
Production of a quality level i item
Formulation as a Markov decision process
We use the uniformization technique
We uniformize the continuous time Markov chain by using the maximum transfer rate v = M1 + 
Stability
Fixed market size M bounds the state space and ensures stability

## Slide 9: Bellman Equations I

## Slide 10: Bellman Equations II
for k > 0 , (x , y) є Z and V0(x , y) = 0 for every (x , y) є Z

## Slide 11: The optimal long-run average profit
We approximate it numerically by the value iteration
algorithm as stated in the following proposition
(Puterman, 1994).
Proposition 1: Suppose that every average optimal stationary deterministic policy has an aperiodic transition matrix, then the long-run average profit rate J* is given by
for every (x, y) є Z and for any V0(x , y)

## Slide 12: Structure of the optimal policy: a numerical example
M | 1 | 2 | μ | r | c | b | i
55 | 1 | 0.1 | 55 | 4 | 4 | 0.35 | 0,…,7
Test example parameters
Quality determined by the absolute deviation of a certain quality characteristic value Y from a target value t
Y follows the normal distribution with mean value t = 10 and variance  2 = 1
We assume linear relationship between quality and satisfaction
quality level i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
pi | 0.261 | 0.234 | 0.188 | 0.135 | 0.087 | 0.050 | 0.026 | 0.019
si | 0.890 | 0.779 | 0.668 | 0.556 | 0.444 | 0.333 | 0.222 | 0.111

## Slide 13: Structure of the optimal policy: a numerical example
Optimal policy (x, y, i) for the two worst quality levels, i  6, 7
For the remaining quality levels i, (x, y, i) = 1, for all system states

## Slide 14: Sensitivity of the optimal policy
Switching curves of the optimal policy for different revenue and rejection cost values
The area on the left of each switching curve corresponds to the optimal scraping decisions and the area on the right to the optimal selling decisions

## Slide 15: Sensitivity of the optimal policy
Switching curves of the optimal policy for different unit backlog cost and regular customers order arrival rate values
The area on the left of each switching curve corresponds to the optimal scraping decisions and the area on the right to the optimal selling decisions

## Slide 16: The optimal policy
Complex structure
Depends on the quality level of the item produced
Depends on the state of the system
There are cases where the results denote that the optimal policy depends only on the quality level
In these cases optimal policy degenerates to a threshold-type policy and the system can be modeled as a closed queuing network (CQN)

## Slide 17: An equivalent Closed Queuing Network
Node 0: exponentially distributed processing times with mean 1/μ and one production station
Node 1: exponentially distributed processing times with mean 1/ 1 and M servers
Node 2: exponentially distributed processing times with mean 1/ 2 and M servers
n0
0
n1
n2
1
2
p00
queue of regular customers: n1  x
p01
p02
queue of occasional customers: n2  M–x–y
backlog: n0  y
n0 + n1 + n2 = M
CQN state: (n0, n1, n2)
q : quality level above which an item is scraped
p00  pq+1 + … + pI

## Slide 18
pkj : routing probabilities
k : service rates of the nodes
  [pkj] : the matrix of routing probabilities
U  [U0 U1 U2 ] any nonnegative solution of the system of linear equations U  U
ak(nk) : the number of occupied servers in node k
a0(n0) = 1 , a1(n1) = n1 and a2(n2) = n2
βk(nk) = ak(nk)βk(nk1), where βk(0) = 1
β0(n0)  1, and k(nk)  nk! for k  1, 2
k  Uk/k, 0 = U0/, ρ1 = U1/1, ρ2 = U2/2
G(M) : a normalization constant given by

## Slide 19
P(n0, n1, n2) : the probability of being in the state (n0, n1, n2) in equilibrium
P0(y) : the probability of n0  y customers awaiting service in node 0
B : the average number of pending orders in node 0
TH0 : the throughput of node 0
TH0 = U0G(M  1)/G(M)

## Slide 20: The average profit rate J
The average profit rate J of the CQN, for a specified threshold q is given by
J = rTH0(1  p00) – bB – cTH0p00
The optimal pair (q*, J*)
Set J*  – and the quality threshold q  0
While q  I
Set q:  q + 1
Compute p00, p01, p02, the equilibrium probabilities and the corresponding J
If J < J*, then we set J*  J and q*  q

## Slide 21: Numerical results
In all numerical experiments presented here the total number of customers is M = 50
We use eight distinct quality levels ( i = 0,…,7 )
The production probabilities pi are based in the same distribution as in the first example mentioned
The conditional probabilities are also the same with those in the first example
Concerning the optimal policy model, in the column “Policy structure” at the results, we present the optimal policies for every quality level. For a certain quality level:
(0) : the optimal decisions are scrapping decision for all states
(1) : the optimal decisions are selling decisions for all states
(\) : there are both scrapping and selling decisions in the state space

## Slide 22: Examples and results for both optimal and threshold policy
Parameter values Optimal policy Threshold policy
1 2  c r b Policy structure Average profit Average profit Quality threshold
__________________________________________________________________________________________ 1 0.1 55 4 4 0.35 111111\\ 51.255383 51.165181 level 5
1 0.1 55 4 4 0.45 111111\\ 51.221129 51.131003 level 5
1 0.1 55 4 4 0.6 111111\\ 51.169754 51.079778 level 5
1 0.1 55 4 4 0.8 111111\\ 51.101278 51.011384 level 5
1 0.1 55 4 4 1.1 111111\\ 50.998663 50.908852 level 5
1 0.1 55 4 4 1.35 111111\\ 50.913222 50.823410 level 5
_________________________________________________________________________________
1 0.1 55 4 3.5 0.35 1111111\ 44.649882 44.575442 level 6
1 0.1 55 4 4.5 0.35 111111\0 57.998738 57.896663 level 5
1 0.1 55 4 5 0.35 11111\\0 64.772343 64.642366 level 4
1 0.1 55 4 5.5 0.35 11111\\0 71.859395 71.718639 level 4
1 0.1 55 4 6 0.35 11111\00 78.949696 78.794912 level 4
_________________________________________________________________________________
1
1 0.1 55 2.2 4 0.35 1111\\00 53.891926 53.424611 level 3
1 0.1 55 2.5 4 0.35 1111\\00 52.836943 52.733324 level 4
1 0.1 55 3 4 0.35 11111\\0 52.087461 51.985423 level 4
1 0.1 55 3.5 4 0.35 1111\\00 70.723484 70.555552 level 3

## Slide 23: Examples and results for both optimal and threshold policy
Parameter values Optimal policy Threshold policy
1 2  c r b Policy structure Average profit Average profit Quality threshold
_________________________________________________________________________________
0.8 0.1 55 4 4 0.35 1111111\ 48.989474 48.913564 level 6
0.9 0.1 55 4 4 0.35 111111\\ 50.202982 50.116805 level 5
1.1 0.1 55 4 4 0.35 111111\\ 52.150325 52.056024 level 5
1.4 0.1 55 4 4 0.35 111111\\ 54.177700 54.073082 level 5
_________________________________________________________________________________
1 0.08 55 4 4 0.35 111111\0 42.697024 42.617049 level 5
1 0.12 55 4 4 0.35 1111111\ 59.191805 59.099059 level 6
1 0.15 55 4 4 0.35 1111111\ 70.133711 70.033063 level 6
1 0.2 55 4 4 0.35 11111111 86.084805 85.982183 level 7
_________________________________________________________________________________
1 0.1 45 4 4 0.35 111111\\ 51.106237 51.016541 level 5
1 0.1 50 4 4 0.35 111111\\ 51.190849 51.100905 level 5
1 0.1 60 4 4 0.35 111111\\ 51.306170 51.215759 level 5
1 0.1 65 4 4 0.35 111111\\ 51.347163 51.256585 level 5
1 0.1 55 4 4 0.35 111111\0 51.576829 51.486063 level 5

## Slide 24: Conclusions
The mean profit rates of the two policies differ by less than 1%
The optimal policy model can be a helpful tool for examining the dynamics of quality in production and the way it affects customer satisfaction, market share and profitability
In cases where this approach is not easy to implement, a simple threshold-type control policy with reasonable computational requirements is proposed and appears to be a good approximation of the optimal policy
As a next step we intend to examine the case where customer satisfaction is affected by his previous state
Another extension is to consider the effect of waiting times in customer satisfaction